## Slide 1: RISC-V: From MIPS to a Modern Open ISA
Tianbo Yang
20721163

## Slide 2: What is RISC-V
What it is
RISC-V is an Instruction Set Architecture (ISA) — a set of instructions that defines how a processor operates.
Licensing
It is open-source and royalty-free, meaning anyone can use it to design processors without paying any licensing fees.
Design Philosophy
It is based on the principles of Reduced Instruction Set Computing (RISC), which emphasizes simple and efficient instructions.
Origin
It was developed by the University of California, Berkeley in the 2010s.
RISC-V is an open-source, royalty-free Instruction Set Architecture (ISA) based on the principles of Reduced Instruction Set Computing (RISC), developed by the University of California, Berkeley in the 2010s.
The interface specification between software and hardware.
CISC
OPPO

## Slide 3: Data Evidence of RISC-V's Rising Popularity

## Slide 4: Reasons Behind the Popularity of RISC-V (Industry)
Open & Royalty-Free
no licensing fees
Any company can implement, manufacture, and sell RISC-V based chips without paying royalties
lowering the barrier to entry especially for startups chip designers.
Better than MIPS and ARM
MIPS and ARM have licensing fees

## Slide 5: Reasons Behind the Popularity of RISC-V (Industry)
Open & Customizable: Modular & Scalable
base + extension design
tailor the architecture precisely to their product needs
without carrying unnecessary hardware overhead.
Selective ALU and Control unit

## Slide 6: Reasons Behind the Popularity of RISC-V (Industry)
Base Integer Instruction Set:
RV32I / RV64I
Embedded: RV32E / RV64E
Common Standard Extensions:
"M" Extension for Integer Multiplication and Division
"A" Extension for Atomic Instructions
"F" Extension for Single-Precision Floating-Point
"D" Extension for Double-Precision Floating-Point
"Q" Extension for Quad-Precision Floating-Point
"C" Extension for Compressed Instructions
“B” Bit Manipulation Extensions
"V" Standard Extension for Vector Operations
(RISC-V International, 2025)
ratified extension that is not yet merged into the published specifications:
e.g. Scenario: An ADAS (Advanced Driver Assistance System) chip
RV64I + M + A + F + D + V + C + H

## Slide 7: Reasons Behind the Popularity of RISC-V (academia)
Open & Customizable: Open Access Open Access for Research Researchers can freely modify and extend the ISA, implement custom microarchitectures, and publish results — without legal or licensing barriers that proprietary ISAs like ARM would impose.
Origin
Born from Academia RISC-V originated at UC Berkeley in 2010, designed explicitly for teaching and research. Its clean, minimal design makes it an ideal subject for studying ISA design principles.

## Slide 8
A 5-Week Teaching Plan
1
Week 1
Introduction to RISC-V & Computer Performance
2
Week 2
3
Week 3
RISC-V Assembly Programming: Control Flow & Procedures
4
Week 4
5
Week 5
Single-Cycle RISC-V Processor Design
RISC-V Assembly Programming: Basics & Operands & Operations
RISC-V Instruction Set Architecture & Encoding
The plan mirrors the structure students know from MIPS, easing the transition while progressively introducing RISC-V's advantages.
Register operands, Memory operands, Immediate operand

## Slide 9
WEEK 1 — ISA COMPARISON
MIPS vs. RISC-V: Foundational Differences
Dimension
MIPS
RISC-V
License & Ownership
Proprietary — requires licensing fees; restricts commercial and academic use
Fully open ISA — free to use, implement, and extend with no licensing fees
Origin
Stanford University, 1981 — pioneered RISC principles
UC Berkeley, 2010 — benefits from nearly 30 years of ISA design hindsight
ISA Structure
Fixed, monolithic ISA — all instructions bundled together
Modular: base RV32I + optional extensions (M, F, C, V) for multiply, float, compressed, vector
RISC-V's modular design means a microcontroller and a supercomputer can share the same base ISA — a key pedagogical and industry advantage.

## Slide 10: Week 2 Different Operands
32 Registers in Register file
MIPS:
RISC-V:
Register Naming
MIPS: $zero, $t0–$t9, $s0–$s7, $a0–$a3, $v0–$v1
RISC-V: x0–x31 with ABI aliases zero, t0–t6, s0–s11, a0–a7
Argument Registers
MIPS: 4 registers ($a0–$a3)
RISC-V: 8 registers (a0–a7) — fewer stack spills in function calls
Saved Registers
MIPS: 8 registers ($s0–$s7)
RISC-V: 12 registers (s0–s11) — more local variable capacity
Operands Key Different:
Register Operands:
Immediate Width
MIPS: 16-bit
RISC-V: 12-bit
Immediate Operands:

## Slide 11: Week 2 Different Operations
Large Immediates
MIPS: li pseudo-instruction hides complexity
RISC-V: Explicit lui + addi — transparent two-step process
RISC-V Large Immediate Example
# Load 0x12345678 into t0
lui t0, 0x12345 # upper 20 bits
addi t0, t0, 0x678 # lower 12 bits
MIPS Equivalent
# Single pseudo-instruction
li $t0, 0x12345678 # assembler expands internally
# Load 0x12345678 into $t0
lui $t0, 0x1234 # upper 16 bits
ori $t0, $t0, 0x5678 # lower 16 bits
RISC-V makes the two-step load explicit — reinforcing how hardware actually handles large constants, a valuable teaching moment.
lui + ori
ori is a pure bitwise operation — it doesn't care whether the top bit is 0 or 1, it just stitches the bits together. addi, however, treats its 12-bit immediate as a signed number. If the top bit is 1, the hardware sign-extends it — filling all the upper bits with 1s — which means the value is interpreted as negative. For example, 0x800 becomes -2048 instead of +2048, making the result 4096 too small.
So how does RISC-V fix this? The assembler handles it automatically. When it sees a lui followed by an addi whose lower 12 bits have a top bit of 1, it quietly adds 1 to the lui value — effectively adding 4096 upfront to cancel out the -4096 that addi will introduce. The result is always correct, and the programmer never has to think about it.
The deeper point here is that RISC-V makes this two-step process visible, rather than hiding it like MIPS does. That transparency is exactly what makes it a better teaching architecture — you can see how the hardware actually handles large constants, step by step.

## Slide 12
WEEK 3
Control Flow & Procedures
Branch Instructions
MIPS provides beq, bne, blt, bgt, ble, bge. RISC-V uses beq, bne, blt, bge, bltu, bgeu — no bgt/ble; swap operands instead.
Comparison Method
MIPS uses slt combined with beq/bne. RISC-V branch instructions directly compare two registers — fewer instructions, cleaner code.
Function Return
MIPS: jr $ra — RISC-V: ret (expands to jalr x0, ra, 0), more descriptive and readable.
Branch Delay Slot
MIPS: Branch instructions have a delay slot — the instruction immediately after a branch always executes regardless of the outcome, forcing programmers and compilers to manually fill this slot or waste a cycle with nop.
RISC-V: No delay slot exists — branches take effect immediately, making code behaviour intuitive and eliminating a legacy workaround that was only needed for 1980s pipeline designs.
RISC-V follows a minimal instruction set philosophy — if an operation can be achieved by reusing an existing instruction with swapped operands, no new instruction is needed. bgt and ble are redundant: swapping the two register operands in blt and bge produces identical behaviour, so RISC-V deliberately omits them to reduce hardware complexity.
e.g.
bgt a, b, L = blt b, a, L ble a, b, L = bge b, a, L
e.g.
MIPS: slt $t0, $s0, $s1
bne $t0, $zero, L
RISC-V: blt x18, x19, L

## Slide 13
WEEK 4
ISA Encoding & Instruction Formats
https://en.wikipedia.org/wiki/RISC-V#ISA_base_and_extensions
https://www.researchgate.net/figure/Three-different-32-bit-instruction-formats-of-MIPS-architecture-37-Rs-Source_fig2_359971270
Instruction Formats
MIPS: 3 formats (R, I, J).
RISC-V: 6 formats (R, I, S, B, U, J) — separating store, branch, and upper-immediate operations.
Opcode Width
MIPS: 6-bit opcode → 64
opcodes.
RISC-V: 7-bit opcode → 128 opcodes, leaving room for future extensions.
Fixed Register Positions
RISC-V: RISC-V keeps rd, rs1, rs2 at identical bit positions across all formats — dramatically simplifying hardware decode logic.
PC-Relative Addressing
MIPS：pseudo-absolute addressing — the jump instruction stores a 26-bit target field, which is combined with the upper 4 bits of the current PC to form a 32-bit address, locking jumps within the current 256MB memory region. j 0x1000_0050 → target = PC[31:28] + 26-bit field + 00
RISC-V: PC-relative addressing — the jump instruction stores only a signed offset from the current PC, so the program runs correctly regardless of where it is loaded in memory. jal ra, foo → target = PC + 0x50

## Slide 14
WEEK 5
Single-Cycle Processor Design
Fetch
PC+4 logic identical in both ISAs.
Decode
MIPS fully decodes before register read; variable fields.
Execute
MIPS uses simple contiguous sign-extension of immediates.
Control
MIPS:6+6 bits; RISC-V:7+3+7 control fields.
MIPS Datapath
Requires full decode before register file read. Simple contiguous immediate fields. Control driven by 6-bit opcode + 6-bit funct.
RISC-V Datapath
Fixed register field positions allow early register read — before full decode completes. Split immediates require reassembly logic. Control uses 7-bit opcode + funct3 + funct7 — more structured and extensible.
e.g.
I instruction
lw $t0, 0($s0) → rt = $t0, bits 20–16, destination (write) sw $t0, 0($s0) → rt = $t0, bits 20–16, source (read)

## Slide 15
RISC-V Teaching Tools
Two open-source simulators for learning and researching the RISC-V architecture — from classroom to lab.
BEGINNER FRIENDLY
RARS
RISC-V Assembler and Runtime Simulator — successor to the MIPS simulator MARS.
License: MIT, free and open-source
Run: java -jar rars.jar (JDK required)
ISA: RV32I / RV64I
Features: code editing, assembly, single-step execution, register & memory visualization
Ideal for: beginners, classroom demonstrations
github.com/TheThirdOne/rars
ADVANCED / RESEARCH
Spike
RISC-V ISA Simulator — official reference simulator by RISC-V International, the industry gold standard.
License: BSD, free and open-source
Platform: Linux / macOS, paired with RISC-V GNU Toolchain
ISA: RV32/64 IMAFDC and all major extensions
Features: ISA verification, GDB debugging, low-level behavior simulation
Ideal for: advanced learners, academic research
github.com/riscv-software-src/riscv-isa-sim
Feature
RARS
Spike
Interface
Graphical GUI
Command-line
Installation
Easy — JDK only
Moderate — build from source
Target Audience
Beginners, students
Advanced learners, researchers
Primary Use
Classroom demos, labs
ISA verification, research

## Slide 16: Reference list
The SHD Group (2024) RISC-V Market Report: Application Forecasts in a Heterogeneous World (Abridged version). SHD101A.b-24. The SHD Group.
RISC-V International. (2021). RISC-V Unprivileged Specification
https://en.wikipedia.org/wiki/RISC-V#ISA_base_and_extensions
https://www.researchgate.net/figure/Three-different-32-bit-instruction-formats-of-MIPS-architecture-37-Rs-Source_fig2_359971270
github.com/TheThirdOne/rars
github.com/riscv-software-src/riscv-isa-sim